## Slide 1: Bioprocessing - A Brief Introduction
Michael P. Rouse Middough, Inc. February 10, 2009

## Slide 2: Bioprocessing: The Integrated Biorefinery

## Slide 3
Fort Calhoun Nuclear Power Plant
Cargill Biorefinery Complex
The Future?
Solid Fuel (Uranium)

Electricity
Solid Fuel (Biomass) + Electricity

Liquid Fuel (Ethanol) + Biochemicals

## Slide 4
Animal Feed
Corn Oil
Products
Milling
Ethanol
Steeping
Corn Receiving
Corn Syrups
Amino Acids
Polyols
Polylactic Acid
Lactic Acid
Enzymes (Future)
Refining
Notes: 4

## Slide 5
Bioprocesses
Corn Steeping
Starch Liquefaction
Saccharification
Ethanol
Lactic Acid
Amino Acids
Enzymes
Anaerobic Biodegradation
Aerobic Biodegradation
Glucose Isomerization

## Slide 6: Bioprocessing: The Basics

## Slide 7: Bioprocess Mechanisms
Live whole cell: used for energy-requiring processes and biodegradation
Dead whole cell: typically used to immobilize enzymes (not common)
Cell-free enzymes: used as homogeneous catalysts - typically hydrolases

## Slide 8: Bioprocess Organisms
Unicellular: bacteria, cyanobacteria, algae, yeast, mammalian cells, plant cells, insect cells
Filamentous: fungi
“Higher life forms”: plants, animals - biopharming

## Slide 9
February 7, 2009
F.D.A. Approves Drug From Gene-Altered Goats
By ANDREW POLLACK
Opening the barn door to a new era in farming and pharmaceuticals, the Food and Drug Administration on Friday approved the first drug produced by livestock that have been given a human gene.
The drug, meant to prevent fatal blood clots in people with a rare condition, is a human protein extracted from the milk of genetically engineered goats.
At the same time, the F.D.A. also approved the goats used to make the drug, the first such animals cleared under guidelines the agency adopted only last month to regulate the use of transgenic animals in the nation’s drug and food supply.
Made by a company called GTC Biotherapeutics, the human anticlotting protein is produced by a herd of 200 bioengineered goats living under carefully controlled conditions on a farm in central Massachusetts.

## Slide 10: Bioprocess Classes
Biosynthesis: Products synthesized by anabolic or catabolic pathways
Biotransformation: Starting compound transformed into new compound via one or more enzymatic reactions
Biodegradation: Feedstocks catabolized into simple, often inorganic, compounds

## Slide 11: Bioprocessing: Some Examples

## Slide 12: Biosynthetic Processes
Primary Metabolites – Live cell processes generally linked to growth:
  Ethanol from glucose: C6H12O6  2C2H5OH + 2CO2 + Energy
  Biogas from cellulose: [C6H10O5]n + nH2O  3nCH4 + 3nCO2 + Energy
  Lactic acid from glucose: C6H12O6  2C2H4OHCOOH + Energy

## Slide 13: Biosynthetic Processes
Lactic acid from glucose - pyruvic acid as an electron acceptor/reducing equivalents sink:
  Glycolysis: C6H12O6 + 2NAD+ + 2ADP + 2Pi     2C2H3OCOOH + 2NADH + 2H+ + 2ATP + 2H2O
  NAD+ Regeneration: 2C2H3OCOOH+ 2NADH + 2H+  2C2H4OHCOOH+ 2NAD+

## Slide 14: Biosynthetic Processes
Secondary metabolites - live cell processes independent of growth:
  Antibiotics: penicillin, erythromycin
  Amino acids: lysine, tryptophan
  Fatty acids: arachidonic acid, docosahexaenoic acid

## Slide 15: Biosynthetic Processes
Secondary metabolites - continued:
  Triglycerides: algae biodiesel
  Polyhydroxyalkanoates: natural polyesters
  Therapeutic proteins: insulin, EPO, “clot busters”, monoclonal antibodies
  Industrial enzymes: amylases, proteases, lipases, cellulases

## Slide 16: Biotransformation Processes
Live whole-cell processes:
  Acetic acid from ethanol: C2H5OH + O2  CH3COOH + H2O + Energy
  Diesel biodesulfurization:
S
+ 3O2 + 4NADH + 4H+
SO2- H+
HO
+ 4NAD+ + 3H2O

## Slide 17: Biotransformation Processes
Live whole-cell processes:
  meta-hydroxyphenylacetylene:
C
CH
HO
C
CH
OH
+ O2 + NADH + H+
+ NAD+
HO
C
CH
OH
BASE 
C
CH
HO
+ H2O

## Slide 18: Biotransformation Processes
Dead whole-cell processes:
  Glucose isomerase: glucose fructose (HFCS)
Enzyme (cell-free) processes:
  Starch liquefaction
  Saccharification
  Cellulose hydrolysis

## Slide 19: Biotransformation Processes
Enzyme (cell-free) processes:
  Laundry stain removal
  Bread staling inhibition
  Lipid hydrolysis
  Transesterification – improvement in vegetable oil properties, conversion of triglycerides to fatty acid methyl esters.

## Slide 20: Bioprocessing: Understanding The Limitations

## Slide 21: Technical Limitations
Biological contamination:
  Difficult to exclude all other microorganisms, phages
  An area not well understood and appreciated by non bioprocess engineers
  Limits most biosynthesis and biotransformation processes to batch

## Slide 22
A Chemical Engineer’s Approach to Milk Production

## Slide 23: Technical Limitations
“Catalyst” is a living organism:
  Easy to kill/inactivate by process upsets
  Slow to grow
  Works only in a narrow range of temperature, pressure, pH, oxygen concentration, etc.
  Shear-sensitive

## Slide 24
The Life of a Bioprocess Engineer
Source: http://www.inflationdata.com/inflation/Inflation_Rate/Historical_Oil_Prices_Table.asp accessed February 10, 2009
Born
High school senior project biogas production
Undergraduate research ethanol production
First job ethanol research
Laid off
Midlife Crisis
Higher value bioproducts
Ethanol plant engineering

## Slide 25
What’s the Point?

## Slide 26: Economic Reality
High capital costs:
  Slow growing/ dilute aqueous batch processes require large/multiple reactors
  Aqueous reaction media require 304/316 stainless steel equipment and piping
  Large, multiple step downstream processing to recover product from dilute aqueous reaction media

## Slide 27: Economic Reality
High operating costs:
  Cells can require expensive media to grow
  Aerobic processes require considerable electric power input for aeration
  Processes require skilled labor 24/7 to operate
  Multiple downstream steps required to recover products from dilute streams

## Slide 28: When to Use Bioprocesses
Chiral compounds: amino, lactic acids
Complex, high-value organic molecules: citric acid, antibiotics, proteins
Highly specific reactions: Starch/ cellulose hydrolysis, hydroxylations
Biodegradation of waste streams: sewage, animal manures

## Slide 29: When Not to Use Bioprocesses
Low value, high volume simple molecules: BTX, ethylene, alcohols
Fuels: ethanol, butanol, diesel
Toxic compounds: phenols

## Slide 30: When to Consider Bioprocesses
Source: http://www.inflationdata.com/inflation/Inflation_Rate/Historical_Oil_Prices_Table.asp accessed February 10, 2009
Here
Here

## Slide 31
Source: Top Value Added Chemicals from Biomass Volume I—Results of Screening for Potential Candidates from Sugars and Synthesis Gas, T. Werpy and G. Petersen, Editors, Pacific Northwest National Laboratory (PNNL) and National Renewable Energy Laboratory (NREL), 2004

## Slide 32: In Summary
Bioprocesses have been and will continue to be important for the production of foods and medicines
Bioprocesses have an uncertain future in the production of fuels
Bioprocesses are likely to become more important in the production of fine and commodity chemicals